## Slide 1: UB Talker
Student Researchers: Dominique Hickson1, Jennifer Barker3, Olivia Spellicy2 ,Jeremy Pettroto1, Megan Yoerg3, MacKenzie Bardsley3, Zachary Salim1, Ian Kaminer1, Michael Mincone1, Arnav Matta5, Corey Ropell1, Devon Rennoldson4, Sriram Subramanian1 Faculty Mentor: Dr. Kris Schindler1
Departments: 1Computer Science and Engineering, 2Communicative Disorders and Sciences , 3Nursing, 4Cognitive Science, 5Mechanical Engineering

## Slide 2: What is UB Talker?
An Augmentative and Alternative Communication (AAC) device requiring little to no physical ability aiding patients with complex communication needs.
Provides a way for patients to construct words and sentences without using their voice.
Speech generating device: Provides Text-to-Speech to verbally hold a conversation
Control various devices (TV, lamp, Call Light, etc.)

## Slide 3: Our former client, Tim
Advanced case of ALS
Complete loss of motor function
Can’t speak or move
Still strong mentally
Tim passed in August 2017

## Slide 4: What is ALS?
Amyotrophic Lateral Sclerosis
Progressive disease that affects all voluntary muscles
Eventually disables the patient’s ability to: move, speak or otherwise communicate, and breathe on their own
Positive: patients will NOT lose control over eye movement
  Eye Tracking technology
ALS has a relatively predictable progression, so communication devices can follow a common trend and be tailored to each individual

## Slide 5: What is a stroke?
When a stroke occurs, blood supply to the brain becomes blocked, killing brain cells.
In some patients this will cause speech and language problems.
Potentially causing one or both types of Aphasia:
Wernicke’s (unable to understand speech) & Broca’s (Unable to produce speech)

## Slide 6
No two patients are the same:
With each patient we get to know their personal needs and wants to create the best form of communication for them.
Important:

## Slide 7: Generations of Devices
Push Button
  Can be used with any body part
  Need sufficient pressure to press
Twitch Switch
  Variable Sensitivity- bend strip
  Limited locations on the body
Eye-Tracking Communication Device (ETCD)
  Detects users pupils, only requires eye movement

## Slide 8: Java Application
Application cycles through options
Peripheral device used to select options
  Cycles through rows
  Cycles through columns
  Selection by mouse click
Advantage: Accurate
Disadvantage: Slow

## Slide 9: Tobii EyeX: How does it work?
PCCR- pupil centre corneal reflection
Near-infrared light is used to illuminate the eyes, and a camera is used to capture images of the reflections
Advanced image processing algorithms are used to calculate and determine the position of the eye and the gaze direction

## Slide 10: ETCD: Application
Only requires eye movement
Exclusively ETCD controlled
Buttons highlight at a glance
Selection made by staring
  Time required for selection is variable
Interface is scalable for ease of use
Phrases can be customized to the user
Can interface with peripheral hardware
  Hospital call light
  TV, lamp, fan

## Slide 11: Design of Server/Client
Server Wrapper
  Launches automatically when the Pi boots up
  Launches a server program as a child process
  If the server quits unexpectedly, reboots Pi
    Quickest way to restore functionality
    Safeguards against resource leaks
Server program
  Receives wireless data from the client on Tim’s tablet
  Spawns an appropriate child process designated by the data
    Protects server if child fails
    Allows for dynamic amount of control

## Slide 12: Design of Server/Client
Client code
  Runs from within UBTalker program
  Will seek out IP address of, and connect to, Pi upon invocation
  Transmission of data consists of no more than a few dozen bytes

## Slide 13: TV Control

## Slide 14: TV Control
Remote device: Raspberry Pi
  LIRC Software
  Mimics remote
  GPIO flashes LED using transistor

## Slide 15: Light and Fan Control
Room Control Button
  Opens submenu with buttons for room control
  TV Control opens menu with TV remote buttons
  “Light On/Off” and “Fan On/Off”
    Sends “lightToggle” or “fanToggle” to Pi
    Program named “lightToggle” or “fanToggle” on Pi flips the output of the respective pin
    Light pin and Fan pin activate or deactivate their respective relays
  On button press, commands are sent from Desktop UI to a remote device via WLAN (IPv4)

## Slide 16: Design of Messaging
Contact List
  Google Drive API
  Contacts in CSV File
Sending Messages
  C# Built in SmtpClient class
There must be a Google Drive that the person managing Tim’s contacts will have access to
In the Google Drive’s root directory, there must be a file named “contacts.csv”
In this file, there should be a single contact on each line in the following format
  <Contact Name>, <Contact Number or Email>
  Phone numbers must 10 digit and have their carrier’s domain appended

## Slide 17: Design of Messaging

## Slide 18: Design of Messaging

## Slide 19: Design of Messaging

## Slide 20: Design of Messaging

## Slide 21: Brain Computer Interface (BCI)
Multiple uses
  Electromyography (EMG)
  Electroencephalogram (EEG)
  Electrocardiogram (EKG)

## Slide 22: Detecting Eye-Blinks
EMG
  Measures muscle movements (eye blink)
  Electrodes placement:
    Above right eye (data)
    Ear lobes (ground)
    Right forearm (filter HR)
    Left wrist (filter HR)
  Isolate spikes to interpret as mouse clicks
  Simple calibration (sensitivity)
  Successfully used with Java application
Consistent Eye- Blink Tracking

## Slide 23: BCI: Current Research
EEG
  Attempting to isolate motor cortex
  Theory: Thought about movement is simpler than thought about words
  Hypothesis: Signals should be simpler to analyze
Thought moves the cursor
  Ex: move arm up == cursor move up
Can be used in conjunction with ETCD software
  User could switch between ETCD and BCI for control

## Slide 24: BCI: Future Goals
EEG - will decipher brain waves involved in speech
  First recognize thought patterns of a letter
  Progress to words
  Ideally a person could think a word and the computer program would speak it aloud
Integrated with other embedded systems
  Smart home applications
    Lights, Locks, TV
  Sending emails and texts with companion software

## Slide 25: Challenges
Keeping a step ahead of the progression of the disease and provide a new or updated version of the technology as needed
Developing machine learning techniques that will be used to train the program to recognize the user’s thought patterns
Brain waves read by the BCI will require more filtering to get a clean signal
  Must isolate the exact brain wave needed for speech and eliminate the rest
Calibration for the software will be extensive and time consuming

## Slide 26: References
A. Chapter, "The ALS Association Greater New York Chapter | New York | New Jersey", The ALS Association Greater New York Chapter, 2017. [Online]. Available: http://als.org/index.php?page=about_als. [Accessed: 11- Apr- 2017].
"How do Tobii Eye Trackers work?", Tobiipro.com, 2017. [Online]. Available: https://www.tobiipro.com/learn-and-support/learn/eye-tracking-essentials/how-do-tobii-eye-trackers-work/. [Accessed: 11- Apr- 2017].
"What are Brainwaves ? Types of Brain waves | EEG sensor and brain wave – UK", Brainworksneurotherapy.com, 2017. [Online]. Available: http://www.brainworksneurotherapy.com/what-are-brainwaves. [Accessed: 11- Apr- 2017].
"OpenBCI - Open Source Biosensing Tools (EEG, EMG, EKG, and more)", Openbci.com, 2017. [Online]. Available: http://openbci.com/?gclid=Cj0KEQjw2-bHBRDEh6qk5b6yqKIBEiQAFUz29gHepd8i1tdJRRL5g8xcUBdc18Lkh5vNFtpH0UMLKXYaAqr38P8HAQ. [Accessed: 11- Apr- 2017].